## Slide 1: The authN and authR infrastructure of perfSONAR MDM
Ann Arbor, MI, September 2008

## Slide 2: Outline
What is MDM perfSONAR?
Which problem has been solved?
The AAI of perfSONAR
Conclusion and future work

## Slide 3: What is MDM perfSONAR?
perfSONAR (Performance focused Service Oriented Network Monitoring Architecture) system
  Is a joint effort of EU-funded IST project GN2-JRA1, Internet2, ESnet and RNP
  Open source development also for other interested networks
  Name reflects the choice of Service Oriented Architecture
  The solution is deployed and further elaborated in
    European Research Backbone GÉANT
    Connected European National Research and Education Networks
    Internet2’ s Abilene network
    ESnet (Energy Sciences network in US)
    RNP (Brazilian NREN)

## Slide 4: What is MDM perfSONAR? Partners
Connect. Communicate. Collaborate

## Slide 5: What is MDM perfSONAR? Overview
The project is divided in two parts
  The web services architecture
    Java & Perl
  Protocols
    Based on the Open Grid Forum Network Measurement Working Group Schemas
It provides
  Performance measurements in a multi-domain environment
  Cross-domain monitoring capability

## Slide 6: What is MDM perfSONAR? Framework
Connect. Communicate. Collaborate

## Slide 7: What is MDM perfSONAR? Services in perfSONAR MDM 3.0
Available services in perfSONAR MDM 3.0
  Lookup Service
  Authentication Service
  Measurement Archive Service
    RRD and SQL versions
  Measurement Point
    SSH/Telnet
    BWCTL
    Command Line
    TC

## Slide 8: What is MDM perfSONAR? Services in perfSONAR MDM 3.0
Web admin interface!

## Slide 9: What is MDM perfSONAR? Services in perfSONAR MDM 3.0
Easy distribution
  WAR files
  RPM & DEB packages
    Also for Tomcat and eXist DB

## Slide 10: Outline
What is MDM perfSONAR?
Which problem has been solved?
The AAI of perfSONAR
Conclusion and future work

## Slide 11: Which problem has been solved?
User groups using perfSONAR
  NOC (Network Operations Center) / PERT (Performance Emergency Response Team) staff
  Project members (e.g. EGEE project)
  End users
  Administrative/non-technical staff
Users accessing perfSONAR services in a multi-domain environment

## Slide 12: Which problem has been solved?
PerfSONAR services have to be protected
  Accepting messages only from allowed users/user groups
  Providing them only the data they need to get
The scenario we had found…
  Different languages for web services
  Different languages for visualization tools
  Different AAIs in each domain
  Not only the common web-based single sign-on solution

## Slide 13: Outline
What is MDM perfSONAR?
Which problem has been solved?
The AAI of perfSONAR
Conclusion and future work

## Slide 14: The AAI of perfSONAR MDM
The Authentication and authorization Service (AS)
  Developed as another perfSONAR service
  It is used by other services for
    Checking whether the user is authenticated
    Checking whether the user is allowed to do an action in a service
    Checking user’s attributes
http://wiki.perfsonar.net/jra1-wiki/index.php/Authentication_Service_resources

## Slide 15: The AAI of perfSONAR MDM
Connect. Communicate. Collaborate

## Slide 16: The AAI of perfSONAR MDM
What does eduGAIN offer perfSONAR?
  An unified framework of digital identity
    URN registry service
    PKI service
    Neutral area of identity providers and messages
      Shibboleth, PAPI, FEIDE, A-Select, …
    MetaData Service
    GÉANT Identity Provider (GIdP) for “homeless”
    Java-based libraries for interacting with eduGAIN components
  Support for our problems! :-)
What does NOT eduGAIN offer perfSONAR?
  An Authentication and Authorization Service

## Slide 17: The AAI of perfSONAR MDM: profiles
Transmission of credentials
  Clients send security tokens representing themselves
  Web Service Security (WS-SEC) standard
Different clients - different profiles
  Automated Client (AC) profile: without human interaction Scripts
  Client in a Web containEr (WE) profile: web-based applications
  User behind a Client (UbC) profile: non web-based applications

## Slide 18: The AAI of perfSONAR MDM: AC profile
Connect. Communicate. Collaborate
Unique and non-transferable ID for each client
  URN obtained from eduGAIN registry service
Private and public key valid in the eduGAIN trust model
  Subject Alternative Name of the cert contains the URN
  Obtained from eduGAIN PKI
Security Token is based on the X.509 certificate

## Slide 19: The AAI of perfSONAR MDM: AC profile
Connect. Communicate. Collaborate
Authentication data included in the SOAP header
  Certificate of the client sent following the X.509 profile of WS-SEC
Generation of the ws-sec element is a proof of the authenticity of the client
Certificate contains the component ID
  It is used for the Subject in the Attribute Request

## Slide 20: The AAI of perfSONAR MDM: UbC profile
Connect. Communicate. Collaborate
A similar case than AC
  An online CA for getting the certficate
    SASL CA

## Slide 21: The AAI of perfSONAR MDM: WE profile
Connect. Communicate. Collaborate
Uses the eduGAIN webSSO profile
SAML assertions contain user’s credentials
Clients must have a pair of keys valid in the eduGAIN trust model
Security Token is based on SAML assertions

## Slide 22: The AAI of perfSONAR MDM: WE profile
Connect. Communicate. Collaborate
Constraints of the relayed-trust SAML assertion
  It must be bound to the client by the H-BE
    User’s credentials legally obtained
  It must be bound to the resource by the client
    Malicious resource cannot re-use it
This SAML assertion contains
  AudienceRestrictionCondition element with the component ID of the resource
  Authentication statement
    ConfirmationMethod element containing the value relayed-trust
    SubjectConfirmationData has the SAML assertion got from the H-BE

## Slide 23: The AAI of perfSONAR MDM: WE profile
Connect. Communicate. Collaborate
Authentication data included in the SOAP header
  Relayed-trust SAML assertion sent following the X.509 and SAML profiles of WS-SEC
Certificate contains the component ID of the client
Subject of the SAML assertion used for requesting its attributes

## Slide 24: The AAI of perfSONAR MDM: the future
Connect. Communicate. Collaborate

## Slide 25: Outline
What is MDM perfSONAR?
Which problem has been solved?
The AAI of perfSONAR
Conclusion and future work

## Slide 26: Conclusion and future work
perfSONAR has a full AAI with “minimal” efforts
  Components for services
  Libraries for services and clients
  They don’t have to understand AA issues…
    … or almost O:-)
UbC profile has to be redesigned
  It uses SASL CA
    Bad choice
  There is a solution on the way
    “eduroam style”
We are working on the authorization part
  Making easy what it isn’t easy
Main goal for the future: the performance

## Slide 27
Thank you for your attention!
Any questions?